## Slide 1
FPGA-Based Network
Intrusion Detection System
Using Quantized Neural Networks & FINN Framework
Minor Project | Electronics & Communication Engineering
NSL-KDD Dataset | Brevitas | FINN Framework | PYNQ-Z2 FPGA
Confidential — Minor Project Presentation

## Slide 2
Problem Statement
⚡
Speed Bottleneck
Traditional NIDS like Snort run on CPUs and cannot keep up with modern high-throughput line-rate network traffic.
🔁
Reactive, Not Real-Time
Software-based systems introduce millisecond-level latency — far too slow to block zero-day attacks at wire speed.
🔋
Power Inefficiency
GPU-based inference for intrusion detection consumes excessive power, making it impractical for edge deployment.
💡 Solution: Push inference onto FPGA using FINN — achieving microsecond latency with minimal power

## Slide 3
Proposed Solution
01
Data
Preprocessing
NSL-KDD
41 features
→
02
Quantized
MLP Training
Brevitas
2/4/8-bit
→
03
ONNX
Export
Model
Portability
→
04
FINN
Compilation
HLS Code
Generation
→
05
FPGA
Deployment
PYNQ-Z2
Board
Key Benefits
⚡ < 10μs inference latency
🧠 On-chip weights — no DRAM
🔋 Low power edge deployment
📈 Line-rate packet classification

## Slide 4
Dataset — NSL-KDD
What is NSL-KDD?
The NSL-KDD dataset is the standard benchmark for network intrusion detection research. It is a refined version of the KDD Cup 1999 dataset with duplicate records removed. • 125,973 training samples • 22,544 test samples • 41 input features per record • Binary labels: Normal vs Attack
Feature Types
Protocol Type:
TCP, UDP, ICMP
Service:
HTTP, FTP, SSH...
Connection Flags:
SF, S0, REJ...
Byte Counts:
src_bytes, dst_bytes
Attack Categories
DoS — Denial of Service
Probe — Port Scanning
R2L — Remote to Local
U2R — User to Root

## Slide 5
System Architecture
Network
Traffic
Raw packets
→
Feature
Extraction
41 features
→
Normalization
& Encoding
Fixed-point
→
FPGA
Accelerator
FINN Dataflow MLP
→
Alert /
Logging
Normal / Attack
AXI-Stream Interface
Inside the FPGA — FINN Dataflow Pipeline
Input Stream
(41 features)
→
MVTU Layer 1
64 neurons | 4-bit
→
MVTU Layer 2
128 neurons | 4-bit
→
MVTU Layer 3
64 neurons | 4-bit
→
Output
Normal / Attack

## Slide 6
FINN Framework — How It Works
Compiler Flow
Brevitas (PyTorch)
↓
ONNX Export
↓
FINN Graph Transforms
↓
HLS C++ Generation
↓
Vivado Synthesis
↓
FPGA Bitstream
Key Concepts
Dataflow Architecture
Each NN layer becomes a dedicated hardware block. Data flows via FIFOs — all layers run concurrently like a deep pipeline.
MVTU — Matrix-Vector Threshold Unit
Core compute primitive. Performs dot product + thresholding. Weights stored on-chip in BRAMs — no external DRAM access.
Folding Factors
SIMD & PE parallelism knobs let you trade off latency vs area vs throughput to fit your FPGA target.
Quantization
Lower bit-widths (2/4-bit) shrink multipliers to LUT-based popcount logic, drastically cutting resource usage.

## Slide 7
Quantized MLP Architecture
Input
Layer
41
neurons
QuantReLU
4-bit
→
Hidden
Layer 1
64
neurons
QuantReLU
4-bit
→
Hidden
Layer 2
128
neurons
QuantReLU
4-bit
→
Hidden
Layer 3
64
neurons
QuantReLU
4-bit
→
Output
Layer
2
neurons
QuantReLU
4-bit
Model Specifications
Parameter | Value
Weight Bit-Width | 4-bit (also tested 2-bit, 8-bit)
Activation Bit-Width | 4-bit QuantReLU
Total Parameters | ~30,000
Optimizer | Adam (lr=0.001)
Training Epochs | 30
Loss Function | Cross-Entropy

## Slide 8
Results — Bit-Width Trade-off Analysis
~98%
8-bit Accuracy
~97%
4-bit Accuracy
~94%
2-bit Accuracy
4×
Memory Reduction
(8→2 bit)
Chart: Accuracy vs Bit-Width
| 2-bit | 4-bit | 8-bit
Accuracy (%) | 94.2 | 97.1 | 98.3
Chart: Memory Usage vs Bit-Width
| 2-bit | 4-bit | 8-bit
Memory (KB) | 7.5 | 15 | 30

## Slide 9
Hardware Resource Utilization (PYNQ-Z2)
Resource | Used | Available | Utilization
LUTs | 12,400 | 53,200 | 23.3%
Flip-Flops (FFs) | 18,600 | 106,400 | 17.5%
BRAMs | 28 | 140 | 20.0%
DSPs | 12 | 220 | 5.5%
Resource Utilization — Visual
LUTs
23.3%
FFs
17.5%
BRAMs
20.0%
DSPs
5.5%
⚡ Estimated Inference Latency: < 10 μs | Throughput: > 100,000 samples/sec | Power: ~1.5W

## Slide 10
Conclusion & Future Work
✅ What We Achieved
Successfully trained a quantized MLP on NSL-KDD dataset achieving ~97% accuracy at 4-bit precision
Demonstrated 4× memory reduction moving from 8-bit to 2-bit with only ~4% accuracy drop
Exported model to ONNX and ran FINN compilation pipeline generating HLS-ready hardware description
Estimated < 10μs inference latency — orders of magnitude faster than CPU-based NIDS
Showed that FPGA-based edge AI is viable for real-time cybersecurity applications
🚀 Future Work
Live Deployment
Connect to actual PYNQ-Z2 board and classify real network traffic in real-time
Multi-class Detection
Extend from binary to 5-class: Normal, DoS, Probe, R2L, U2R
Mixed Precision
Apply different bit-widths per layer for better accuracy-resource balance
Modern Dataset
Evaluate on UNSW-NB15 or CIC-IDS2018 for more realistic threat scenarios

## Slide 11
Thank You
Questions & Discussion
NSL-KDD
Brevitas
FINN
FPGA
Quantization
Dataflow Architecture